## Slide 1: ET4171 Processor Design Project
LEON3 processor optimization
Group 1:
Luca Feltrin
Henrique Dantas

## Slide 2: Objectives
Target: Embedded applications
  Compound metric: P*BS
Poor Mul/Div execution time
  Implementation with different algorithms

## Slide 3: Multiplier

## Slide 4: Divider
Which algorithm?
  Repeated Multiplication Fast Area
  Reciprocation Fast Area
  Array Divider No control on physical placing
  Radix >8 Fast Area
  Radix-4 Good compromise:
  Execution time ~ ½ of the baseline

## Slide 5: Divider

## Slide 6: Divider

## Slide 7: Divider
Signed division (signed p-d plot) vs. Unsigned division (half p-d plot) + 1 cycle for sign
  No area differences but 1 more cycle delay: signed Division

## Slide 8: Divider
Baseline vs. Radix-4: 19 cycles vs 36

## Slide 9: Synthesis Results
Area, Power, Frequency
 | Clk freq [MHz] | LUTs | Slices | Quiescent Power [W] | Dynamic Power [W] | Total Power [W] | P/f [W/MHz]
Baseline | 80,522 | 9904 | 16889 | 2,467 | 0,721 | 3,188 | 0,03959
Modified | 80,535 | 10479 | 17865 | 2,468 | 0,743 | 3,211 | 0,03987

## Slide 10: Benchmarks Scores
 | Stanford [sec] | Whetstone [sec] | Gmpbench Multiply [Op/sec] | Gmpbench Divide [Op/sec] | Gmpbench RSA [Op/sec] | Division [sec] | Mibench JPEG (average) [sec] | SSD [sec] | Total [sec]
Baseline | 2,30 | 116,2 | 781 | 15876 | 5123 | 8,06 | 23,215 | 10,59 | 219,28
Modified | 2,26 | 113,25 | 801 | 16335 | 5284 | 7,65 | 22,465 | 10,21 | 213,30
Only slight improvement probably due to the Operative System’s Scheduling

## Slide 11: Conclusion
Comparison with metrics
Version | Primitive metrics |  |  |  | Composite metrics |  |  | 
 | A (*10^4) | D (*10^-2) | P | BS (*10^2) | A*D (*10^2) | A*BS (*10^6) | P*D (*10^-2) | P*BS (*10^2)
Baseline | 2,68 | 1,24 | 3,19 | 2,19 | 3,33 | 5,88 | 3,96 | 6,99
Modified | 2,83 | 1,24 | 3,21 | 2,13 | 3,52 | 6,05 | 3,99 | 6,85
Improvements | 5,8% | - | 0,7% | -2,7% | 5,8% | 2,9% | 0,7% | -2,0%

## Slide 12: Furhter Improvements
Cache size
  More power consumption, need to determine actual miss rate
Branch prediction
  Now: Static prediction, only slight advantage, power consumption
Out of Order Execution
  Radical change of the integer unit, improved execution time